## Slide 1: ACTIVITY RECOGNITION IN SMART HOME ENVIRONMENTS
CS 284 Mini Project Presentation by Inna Calimbahin and Isabelle Tingzon

## Slide 2: ACTIVITY RECOGNITION FOR HEALTH MONITORING
Activities of daily living (ADLs) are good indicators of elderly health status.
Smart home environments are capable of monitoring activities performed by its inhabitants.
Activity Recognition is a key component in automated health monitoring.

## Slide 3: In our study, we use CRFs and HMMs for activity recognition in smart home environments;
we compare their performances with other classifiers i.e. SVM, Decision Trees, and Gaussian Naive Bayes classifier.

## Slide 4: SENSOR DATA
is composed of temporal data generated by a set of binary sensors installed in a home environment.
Types of sensors in OrdonezA:
  PIR: Shower, Basin, Cooktop
  Magnetic: Main door, Fridge, Cabinet, Cupboard
  Flush: Toilet
  Pressure: Seat, Bed
  Electric: Microwave, Toaster
Fig 1. Home Settings Description

## Slide 5: SENSOR DATA
is composed of temporal data generated by a set of binary sensors installed in a home environment.
Types of sensors in OrdonezB:
  PIR: Shower, Basin, Door Kitchen, Door Living, Door Bedroom
  Magnetic: Main door, Fridge, Cupboard
  Flush: Toilet
  Pressure: Seat, Bed
  Electric: Microwave
Fig 1. Home Settings Description

## Slide 6: SENSOR STREAM DISCRETIZATION
Sensor stream data is discretized into time slices of constant length .
A binary sensor event in time slice is denoted as indicating whether sensor fired at least once between times and .
For sensors, a binary observation vector can be defined for each time slice.
Fig 2. Temporal segmentation

## Slide 7: SENSOR DATA: DAY AND TIME
Apart from the actual sensor events, the time of day and day of the week that the events occur are also considered valuable features.
Time of Day - values are binned into the following hour ranges:
  0-5 (early morning), 5-10 (morning), 10-15 (afternoon), 15-20 (evening), 20-24 (late evening)
Day of the week – can be represented by a unique identifier

## Slide 8: SENSOR DATA
We obtain an observation vector for each time slice
  - day of the week, and is the time of the day of time slice t.
The activity label in time slice is denoted by for possible labels.
Sequential prediction task is to find the appropriate mapping between:
  input sequence:
  output sequence:
  for a total of time slices.

## Slide 9: ACTIVITY LABELS
← Unlabelled data

## Slide 10: CONDITIONAL RANDOM FIELDS

## Slide 11: EXPERIMENTAL SETUP
Sensor data stream were segmented into time slices of length seconds.
After segmentation,
20,455 time slices for OrdonezA
30,469 time slices for OrdonezB
If we remove unlabelled/“Idle” data:
19,629 time slices for”OrdonezA”
27,235 time slices for dataset ”OrdonezB”.

## Slide 12: FEATURE REPRESENTATION
Raw sensor representation -produces sensor data as it was received from the WSN, i.e. value is 1 if sensor is active, else 0.
Last sensor representation – indicates which sensor fired last.
  The sensor that changed its state last continues to produce a 1 and only changes to 0 when another sensor changes its state to 1.

## Slide 13: PERFORMANCE MEASURE: F-MEASURE
nature of the dataset → severe class imbalance
Accuracy is not a suitable performance measure.
F-Measure considers correct classification of each class as equally important.

## Slide 14: VALIDATION
Leave-one-day-out approach
  takes one full day of sensor readings as the test set and uses the remaining sensor readings as the training set.
  process is repeated for all the days and reports the average F-Measure over the total number of days
  OrdonezA – 14 days
  OrdonezB – 21 days

## Slide 15: RESULTS (ORDONEZA)

## Slide 16: RESULTS (ORDONEZB)

## Slide 17: CONCLUSION
Overall, CRFs outperform the other machine learning methods for both datasets “OrdonezA” and “OrdonezB”
  the highest F-Measure being 82.83%
Higher performance measures are achieved for datasets with only labelled data than datasets with unlabelled data.
We conclude that CRFs and HMMs are effective in classifying activities of daily living based on binary sensor stream data.